进口笔式PH计VSp6-S1

PH测试笔是采用最新微功耗积体电路设计，性能优越，广泛应用于理化分析,

环保，食品，化妆品，水族馆，养殖业，无土栽培…等等行业。

| 优点： | 技术性能： |
| --- | --- |
| ·全防水，IP67等级。 | ·测量范围：0~14pH |
| ·可更换电极。 | ·精确度：±0.1pH |
| ·超大荧幕显示。 | ·环境温度：0℃~50℃ |
| ·携带轻便。 | ·电池：纽扣电池1.5V×3 |
|  | ·仪器尺寸：170mm×37mm×37mm |
|  | ·仪器净重：80g |

- 仪器校准：打开PH笔顶盖，调校调节器

- 将电极放入PH7.0的缓冲溶液中，调校右边调节器，使仪器显示为7.0.

- 将电极放入清水中清洗。

- 将电极放入PH4.0的缓冲溶液中，调校左边调节器，使仪器显示为4.0.

5. PH测试笔在出厂时已校准，可直接使用。（长期久置不用，请于使用时重新校准）

6. 测量后电极应用干净水清洗。当仪器显示屏变暗时，请更换电池及注意电池正负极方向。

7. 将电极保护盖取下，打开电源开关。

8. 将电极放入测试液体中，仪器便会显示准确PH读数。

9. 测量完毕，关闭电源，套上电极保护盖。

PH PEN/Tester Operation Manual

PH PEN/Tester adopted with latest micro-electronic circuit design, to provide high performance, steady and accuracy measurement. This PEN is widely applies in work of chemical analysis, environmental protection, food, hygiene, aquaculture and horticulture, etc.

| Advantage | Specification |
| --- | --- |
| ·Waterproof Class IP67 | ·Testing Range: 0.0pH to 14.0pH |
| ·Replaceable Electrode | ·Accuracy: ±0.1pH |
| ·Large LCD display | ·Ambient temperature:0℃ to 50℃ |
| ·Extremely portable | ·Battery: LR44×3 |
|  | ·Dimension: 158mm×30mm×30mm |
|  | · Weight : 67g |

Instrument Calibration

Maintenance

         If the instrument has not been operating for a long time, it should be recalibrated before use.

         Usually clean the electrode with distilled water after use.

         Replace the batteries when the display became dim.