| 文件名称: | 产品规格书 |
| --- | --- |
| 设备名称: | 剥离试验机 |
| 设备型号: | YL-S90 |

广东越联仪器有限公司

地址：东莞市南城区天安数码城A区1115号

TEL：0769-85842789 85648168

FAX：0769-82287448

E-mail：amy.lian@yuelian-china.cn

| 业务员： | 练小姐 | 手机： | 13580887172 |
| --- | --- | --- | --- |
| 邮箱： | amy.lian@yuelian-china.cn | 网址： | http://www.yuelian-china.cn |

- 产品概述

## 用途：

本机可测试金属、橡胶、塑料、纺织、皮革、纸类、复合材料..等等之拉伸、压缩、粘接力、剥离、撕裂等，新开发的B型显示器操作方式在搭配机型上也 最具弹性，并具数据输出可和专用软件连接可在电脑中做分析、统计、储存等功能。操作简单，本机传动效率高达85%以上，能量损失小精准高，扩充性大可单机 操作也可与电脑连接使用。 This tester is designed for conduct tensile, compression, bending, shearing, bonding strength, peeling, tearing and other tests for rubber, plastic, leather, metal, nylon line, fabric, paper, aviation, packaging, construction, petrifaction, electrician, vehicle and other materials. It is a basic equipment of quality control, receiving inspection, physical test, mechanics research, material development.

功能：

可进行拉力、压力、剥离、撕裂、剪切、环形初粘…等测试 可同时显示力量及位移 采用步进马达驱动,精密滚珠丝杆传动，可直接设定试验速度 上下微调开关，具测试完成,自动回位功能 快拆式接头,能使用各种不同之夹具 单键测试功能,操作简便 可直接连接打印机,输出报表 可单机操作也可与电脑联机操作,USB接口，进行数据分析。

- Can conduct tensile, compression, peeling, tearing, shearing, ring initial adhesion and other test

- Can display force and displacement at the same time

- Adopt stepper motor drive, precision ball screw drive, set test speed by computer directly.

- Up & low fine-turning switch, automatic back after test finished

- Quick-release connector, can use various grips

- All computerized operation, USB interface, conduct data analysis

符合标准：

GB/T2792，ASTM D3330，GB/T 12914-1991，GB 13022-91，GB/T1040-92，GB2792-81，GB/T 14344-9，GB/T 2191-95，QB/T 2171-95

技术参数：

| 型号： Moedel | YL-S90 |
| --- | --- |
| 容量选择: Capacity: | 10N、20N、50N、100N、200N、500N、1KN、（选配一组） |
| 显示器: Display: | 电脑显示方式 Computer display mode |
| 力量分辨率: Force Resolution: | 1/500,000 |
| 力量精度: Force Accuracy: | 0.3% |
| 行程分辨率: Stroke Resolution: | 1/500,000 |
| 控制方式: Control Mode: | 全电脑操作方式 All computerized operation mode. |
| 实验行程: Test Stroke: | 500mm |
| 实验宽度: Test Width: | Ø140mm |
| 实验速度: Test Speed: | 0.5～600mm/min 电脑设定, 附夹具上下快速调节按钮 0.5~600mm/min, can set by computer, with up & down fast adjustment button of grips |
| 力量单位转换: Force Unit Switch: | kgf，N，Ibf，g，ton，Mpa |
| 停机模式: Stop Mode： | 过载停机、紧急停止键、试件破坏自动停机、上下限设定自动停机、自动复位功能，可进行持拉或持压试验。 Overload stop, emergency stop button, specimen damage automatic stop, upper & lower limit set automatic stop, automatic reset function |
| 机台尺寸: Machine Dimension： | 40×30×92cm (W×D×H) |
| 机台动力: Machine Drive: | 步进马达驱动，同步轮及精密滚珠丝杆传动 Stepper motor drive, synchronous wheel and precision ball screw drive |
| 功率: Power: | 180W |
| 机台重量: Machine Weight: | 28kg |
| 使用电力: Power Supply: | 220V 50/60HZ 10A |
| 标准配置: Standard Device: | 夹具1组、电脑软件、USB232电脑连线； 1 set of grips, computer software, USB computer connection wire |
| 选购: Optional: | 个人电脑 Personal computer |