FlawScout

Laser Shearography Non- Destructive Testing (NDT) System

The FlawScout is a fully integrated, non- destructive testing (NDT) system, incorporating the latest in Laser Shearography technology. The FlawScout is designed to be used for quality control and NDT training of up to 430 mm x 400 mm / 17 ’’ x 17 ’’sections. Idealized as a cost-effective solution for primarily fixed-setup applications, the FlawScout is ideal for parameterization of NDT test procedures.

All of Dantec Dynamics’ Laser Shearography products are designed to provide NDT users with unmatched resolute imaging and reliable inspection results. This ensures that for whatever application where quality control is of upmost importance; technicians, engineers and managers alike can all rest assured that safe and true testing conditions are a provision.

Figure 1 - FlawScout Schematic #1

| The software of the FlawScout, Istra4D, includes a new phase-shifting imaging algorithm that yields de-sensitized phase maps. Resolving the phase from four consecutive images promotes desensitization of unclean images from the measurement result. A temperature-compensated phase shifter accommodates elevated environmental conditions yielding reproducible factory-setting conditions. In combination with a 2.0 Mpx CMOS GigE connection with a maximum frame rate of 37 Hz, the FlawScout will always deliver reliable inspection results. | Figure 2 - FlawScout Phase Map |
| --- | --- |

FlawScout & Istra4D Features

|  | High-Resolution imaging Via a 2.0 Mpx, CMOS camera with a maximum frame rate of 37 Hz. |  |  | Automatic shearing control Using Istra4D, the shearing piezo can be fully controlled for shear distance |
| --- | --- | --- | --- | --- |
|  | 4+4 resolved phase maps Using advanced 4+4 image processing algorithms and phase-stepping technology. |  |  | Advanced filtering options For filtering out noise and de-correlation, but also for increasing test sensitivity. |
|  | Custom reporting tool Allows users to export a report based on a custom definable template with selectable fields. |  |  | Recording procedure editor* Allows users to create, load and save recording procedures with comprehensive triggering. |
|  | Referencing, refresh and save Allows users to take a cleared reference images to be compared against snapshots. |  |  | Export movie files Allows users to export individual saved measurement series as a sequence in *.avi format. |
|  | Simple projection calibration Allows users to manually compute and scale the image projection |  |  | Accumulated display imaging Using accumulated step image subtraction, decorrelation is minimized. |
|  | Recording procedure logger* Allows users to log a manual test measurement in the Recording procedure editor. |  |  | Diverse illumination settings Including; optimal camera shutter speed finder, gain control and laser diode output. |
|  | Overlay display Presents an overlay of the live image and phase map for direct marking of defects on samples. |  |  | Export image files Allows users to export images in Bitmap (*.bmp), JPEG (*.jpeg) or PNG (*.png) format. |
|  | Defect and distance marking Allows users to accurately mark, gauge and annotate; single or multiple defects. |  |  | Line segment markers Profiles the phase of measurements for improved visualization of fringes. |
|  | Heat excitation control* Allows users to manually or automatically switch the heat lamps On or Off via Istra4D. |  |  |  |

Customer Service Benefits

|  | Free and unlimited Istra4D evaluation licenses and 1-year free software updates |  |  | 1-year free access to the Laser Shearography User Application Module via the Dantec eLearning platform |
| --- | --- | --- | --- | --- |
|  | Free online support via TeamviewerTM and free E-mail and telephone support. |  |  | Certificate of Calibration: Phase-Shifter and Automatic Shearing |
|  | 1-year warranty (standard) |  |  | Access to a yearly servicing package at a fixed price, including Istra4D software upgrades. |

*Requires DSM 32130: ISTRA 4D Measurement & Control Software Module