名称: 防水卷材拉力试验机

其他名称：电子A试验机,电子拉力试验机

型号：WDW-5

荣计达产品编号：FS02   36000元

防水卷材拉力试验机广泛应用于高分子材料、防水卷材、砂浆建材、塑料橡胶、电线、电缆、纺织、工程塑料、陶瓷、金属材料、食品医药包装等行业的力学分析检测。

Waterproof coil tensile testing machine is widely used in the mechanical analysis and testing of polymer materials, waterproof coiled materials, mortar building materials, plastic rubber, wire, cable, textile, engineering plastics, ceramics, metal materials, food and pharmaceutical packaging and other industries.

防水卷材拉力试验机配置专用夹具可用于干粉砂浆、保温砂浆、防水卷材、石膏、油漆涂料、人造板材、电子元件，纸张布匹的拉伸、压缩、弯曲、剪切、剥离、撕裂等多项物理力学性能试验。配置品牌电脑、中文WINDOWS XP 用户界面、菜单提示、鼠标选择操作，数据和曲线随试验过程动态显示。简单方便。

Waterproof coil tensile testing machine configuration special fixture can be used for dry mortar, thermal insulation mortar, waterproof membrane, plaster, paint coating, artificial board, electronic components, paper fabric stretching, compression, bending, shearing, peeling, tearing, etc. A number of physical and mechanical properties test. Configure the brand computer, Chinese WINDOWS XP user interface, menu prompts, mouse selection operation, data and curves dynamically displayed with the test process. easy and convenient.

防水卷材拉力试验机技术参数

★大试验力KN：5、10、20、50（可根据用户要求定制）

★高精度传感器精度：±0.5%

★负荷精度：±1% 分辨率1/20000码

★速度精度： ±0.5%

★速度范围：0.05-500mm/min （1T以上:1-250mm/min） 或根据用户要求设置

★位移测量精度0.1mm

★大变形测量范围：标线-1000mm（选配）

★移动横梁有效行程：1000mm 可根据用户要求制造不同的拉伸空间

★位移精度：示值相对误差±0.5%

★电源：AC220V  50Hz

★外形尺寸700*380*2150mm（长*宽*高）

★净重：320kg

Waterproof coil tensile testing machine technical parameters
★ Large test force KN: 5, 10, 20, 50 (can be customized according to user requirements)
★High precision sensor accuracy: ±0.5%
★Load accuracy: ±1% resolution 1/20000 yards
★Speed accuracy: ±0.5%
★Speed range: 0.05-500mm/min (1T or more: 1-250mm/min) or set according to user requirements
★ Displacement measurement accuracy 0.1mm
★ Large deformation measurement range: marking line -1000mm (optional)
★ Effective travel of moving beam: 1000mm Different stretching space can be made according to user requirements
★ Displacement accuracy: relative error of indication value ±0.5%
★Power supply: AC220V 50Hz
★Dimensions 700*380*2150mm (length * width * height)
★ Net weight: 320kg

防水卷材拉力试验机软件性能及特点

★配品牌电脑、中文WINDOWS XP 用户界面、菜单提示、鼠标选择操作，简单方便。

★显示方式：数据和曲线随试验过程动态显示。

★自动换挡：根据负荷大小自动切换到适当量程，以确保测量数据的精度。

★控制过程：试验过程及测量、显示、分析、打印等功能均由微机完成

★曲线方式：拉伸：力—伸长、应力-应变、强度-时间；力-时间、伸长-时间、应变-时间。压缩：

力-变形、应力-应变、强度-时间、力-时间、变形-时间、应变-时间 抗弯：力-挠度、强度-时间、力-时间、挠度-时间。

★曲线对比：同组试验的曲线可以多种颜色迭加对比。

★局部放大试验：曲线上的任意段可进行区域放大分析。

★数据分析：在曲线图上的试验数据可随意选取分析。

★报告选择：可按用户需求选择不同的报告格式，可用EXCEL或Word。直接查看报告或取部分打印

★试样选定：一组试样结果可选定有效试验，并可连续测试

★自动存储：试验条件、测试结果、测试曲线和数据可自动存储，随时调用。

★断裂停车：试样拉断瞬间能停车或返回初始位置。

★自动保护：有自动过负荷、过流、过压、欠压、上下限位保护。

★自动返回：移动横梁可设定不同速度，能准确的自动返回到试验初始位置.

★控制功能：具有恒速控制方式。

★可选择不同的力值单位（N、kgf、gf）

★打印：能对试验数据处理、存储、打印、绘制曲线，并打印好报告单，也可集中或分开打印。

★自动校准：对负荷、伸长可用电标定值自动标定。

★清零：可对负荷、变形、位移测量随时进行手动或自动清零。

Waterproof coil tensile testing machine software performance and characteristics
★With brand computer, Chinese WINDOWS XP user interface, menu prompts, mouse selection operation, simple and convenient.
★ Display mode: data and curves are displayed dynamically with the test process.
★Automatic shifting: Automatically switch to the appropriate range according to the load size to ensure the accuracy of the measured data.
★ Control process: test process and measurement, display, analysis, printing and other functions are completed by microcomputer
★ Curve mode: Stretch: force - elongation, stress - strain, strength - time; force - time, elongation - time, strain - time. compression:
Force-deformation, stress-strain, strength-time, force-time, deformation-time, strain-time bending: force-deflection, strength-time, force-time, deflection-time.

★ Curve comparison: The curves of the same group of tests can be superimposed and contrasted in multiple colors.
★ Partial magnification test: Any segment on the curve can be used for regional magnification analysis.
★ Data analysis: The test data on the graph can be selected and analyzed at will.
★Report selection: You can choose different report formats according to user needs, available EXCEL or Word. View reports directly or take partial prints
★ Sample selection: a set of sample results can be selected for effective testing and continuous testing
★Automatic storage: Test conditions, test results, test curves and data can be automatically stored and called at any time.
★ Breaking parking: The sample can be stopped or returned to the initial position when it is pulled off.
★Automatic protection: automatic overload, overcurrent, overvoltage, undervoltage, upper and lower limit protection.
★Automatic return: The moving beam can be set to different speeds and can automatically return to the initial position of the test accurately.
★ Control function: with constant speed control.
★Select different force units (N, kgf, gf)
★Print: It can process, store, print, draw curves for test data, and print perfect report sheets, or print them in a centralized or separate manner.
★Automatic calibration: Automatic calibration of the available electrical calibration values ​​for load and elongation.
★Clearing: Manual or automatic zeroing can be performed on load, deformation and displacement measurement at any time.

防水卷材拉力试验机工作条件

★环境温度在10－30℃之间

★相对湿度≤80％

★在稳固的地基或工作台上，正确安装

★周围无振动源和腐蚀性物质

★电源电压的波动范围不应超过额定电压的±5％

Waterproof coil tensile testing machine working conditions
★The ambient temperature is between 10-30 °C
★ Relative humidity ≤ 80%
★ Install properly on a stable foundation or workbench
★No vibration source and corrosive substances around
★ The fluctuation range of the power supply voltage should not exceed ±5% of the rated voltage

防水卷材拉力试验机结构特点和工作原理：

本机主要由机械和电器两大部分组成。

1、机械部分的结构和工作原理

采用机械加载，由电机驱动减速机，动力传动丝杠带动中间横梁上下移动，中横梁上面及上横梁下面装有两个夹具，实现对试件的拉伸,压缩试验。

2、测量部分的特点和工作原理

采用电脑控制、高精度荷重元、高精度AD转换及进口光电编码器，具有显示直观、操作方便、数据准确等特点。提供现场标定和峰值保持功能。

工作原理如下：试验机加荷使传感器受力产生电信号并送入AD转换器，同时丝杠转动带动编码器产生脉冲信号一起输入微电脑，经控制调整后将试验结果在微机屏上显示出来。

Structural features and working principle of waterproof coil tensile testing machine:
This machine is mainly composed of two parts of machinery and electrical appliances.
1. Structure and working principle of mechanical parts
The mechanical drive is used to drive the reducer by the motor. The power transmission screw drives the intermediate beam to move up and down. Two clamps are mounted on the upper beam and the upper beam to realize the tensile and compression test of the test piece.
2, the characteristics of the measurement part and working principle
It adopts computer control, high-precision load cell, high-precision AD conversion and imported photoelectric encoder. It has the characteristics of intuitive display, convenient operation and accurate data. Field calibration and peak hold are available.
The working principle is as follows: the load of the test machine causes the sensor to generate an electric signal and send it to the AD converter. At the same time, the screw rotates to drive the encoder to generate a pulse signal and input it into the microcomputer. After the control is adjusted, the test result is displayed on the screen of the microcomputer.

防水卷材拉力试验机安装与调整：

1、把试验机从包装中取出，检查试验机在运输中有无碰撞，损坏现象

2、把试验机放在坚固的平台或桌面上，用水平仪找正使仪器处于水平位置。

3、检查供电电压是否为AC220V，电压差不低于标准电压的±5％,电源线必须接地

Waterproof coil tensile testing machine installation and adjustment:
1. Take the test machine out of the package and check whether the test machine has collision or damage during transportation.
2. Place the test machine on a sturdy platform or tabletop and use a level to align the instrument in a horizontal position.
3. Check if the power supply voltage is AC220V, the voltage difference is not less than ±5% of the standard voltage, and the power cable must be grounded.