名称: 高精度铆钉拉拔仪

其他名称：饰面砖粘结强度拉拔仪，粘结强度拉拔仪，保温钉强度拉拔仪

型号：MD-6S

荣计达产品编号：SJ13   3800元

一、产品简介：

铆钉拉拔仪是我公司推出的一款适用于建筑工程固定隔热保温材料铆钉拉拔力、墙体隔热保温材料粘结强度的仪器，采用高精度传感器、机电一体化设计，有功能强大、重量轻、手柄操作省力、简单等特点。产品采用S型高精度传感器、机电一体化设计，全套仪器为一个整体，手柄、S型传感器、丝杠、反力之座机械部分构成一个"门"是结构，数显表，可直接读取拉力值（kN）和强度值(Mpa)，自动计算、峰值保持、存储和查询功能，特别适合试验室和现场使用，全套检测仪具有功能强大、重量轻、手柄操作省力、简单等特点。

The rivet puller is an instrument developed by our company that is suitable for the rivet pull force of fixed heat insulation materials in construction engineering and the bonding strength of wall heat insulation materials. It adopts high-precision sensors and a mechatronics design with powerful functions. , Light weight, labor-saving and simple handle operation. The product adopts S-type high-precision sensor and mechatronics design. The whole set of instruments is a whole. The handle, S-type sensor, lead screw, and reaction seat mechanical parts form a "door" structure. The digital display can be directly read. Tension value (kN) and strength value (Mpa), automatic calculation, peak holding, storage and query functions, especially suitable for laboratory and on-site use. The complete set of detectors has the characteristics of powerful functions, light weight, labor-saving and simple handle operation.

二、技术参数：

★仪器结构：一体式

★显示模式：力值KN /强度值Mpa可调

★测量范围：0-6.000KN /3.75Mpa

★分辨率：0.001KN

★测试精度：0.5%F.S

★峰值保持、液晶照明

★数据存储：500条

★数值修正：10段折线

★供电方式：高容量锂电

★拉拔行程：65mm

★主题材质：轻质合金

★主题重量：2.8Kg

2. Technical parameters:

★Instrument structure: integrated

★Display mode: force value KN/strength value Mpa adjustable

★Measuring range: 0-6.000KN /3.75Mpa

★Resolution: 0.001KN

★Test accuracy: 0.5%F.S

★Peak hold, LCD lighting

★Data storage: 500 items

★Numerical correction: 10-segment polyline

★Power supply mode: high-capacity lithium battery

★Drawing stroke: 65mm

★Subject material: light alloy

★Theme weight: 2.8Kg

三、产品特点：

★一体化设计、轻质合金主体，

★配有内置数显仪表，采用S型高精度传感器；

★设置菜单，数据可记录、查询、删除操作；

★超低功耗设计，无操作自动关机，连续工作时间可超过200 小时；

★强度Mpa和力值KN两种测量模式。

3. Product features:

★Integrated design, light alloy body,

★Equipped with built-in digital display instrument, using S-type high-precision sensor;

★Setting menu, data can be recorded, inquired, and deleted;

★Ultra-low power consumption design, automatic shutdown without operation, continuous working time can exceed 200 hours;

★Two measurement modes of strength Mpa and force value KN.

四、符合标准：

JGJ144-2004《外墙外保温工程技术规程》

JG158-2004《胶粉聚苯颗粒外墙外保温系统》

JG149-2003《膨胀聚苯板薄抹灰外墙外保温系统》

JGJ110-2008《建筑工程饰面砖粘结强的检验标准》

JGJ126-2000《外墙饰面砖工程施工及验收规程》

Fourth, meet the standards:

JGJ144-2004 "Technical Specification for External Thermal Insulation Engineering of External Walls"

JG158-2004 "Adhesive Polystyrene Particle External Wall External Insulation System"

JG149-2003 "Expanded polystyrene board thin plaster external wall external insulation system"

JGJ110-2008 "Inspection Standard for Bonding Strength of Facing Bricks in Construction Engineering"

JGJ126-2000 "Outer Wall Facing Brick Engineering Construction and Acceptance Regulations"

五、产品配置：

★ 拉拔仪主机1台

★ 充电器和USB充电线各1个

★ 试块40*40mm和100*100mm各3块

★ 铆钉拉拔头6/8/10mm各1个

★ 便携式仪器箱

★ AB胶1盒

★说明书、保修卡、合格证各1份

5. Product configuration:

★ 1 host of drawing instrument

★ 1 charger and 1 USB charging cable

★ 3 pieces each of 40*40mm and 100*100mm test blocks

★ 1 rivet drawing head 6/8/10mm each

★ Portable instrument case

★ 1 box of AB glue

★One copy each of manual, warranty card, and certificate