名称: 智能粘结强度检测仪

其他名称：砂浆粘结强度检测仪，砂浆粘结强度拉拔仪,饰面砖粘结强度检测仪

型号：LB-6S

荣计达产品编号：SJ14   3500元

一、产品简介：
采用为便携式液压千斤顶，加压装置与空心千斤顶采用一体式结构设计，便于携带和试验，仪器主体采用超轻主体仅重2.0kg，显示仪表和仪器主体采用一体化设计，无需连接仪表，开机直接测量，仪表显示单位有两种方式KN和MPA可以转换，方便客户使用，使现场检测更加方便快捷。
Product introduction:

Adopted as a portable hydraulic jack, the pressure device and hollow jack adopt an integrated structure design, which is easy to carry and test. The instrument body uses an ultra-light body weighing only 2.0 kg. The display instrument and the instrument body adopt an integrated design. There are two ways to measure and display the unit of the meter. KN and MPA can be switched, which is convenient for customers to use, and makes on-site testing more convenient and quick.
二、技术参数：

| 仪器结构 | 一体式 |
| --- | --- |
| 测量范围 | 0-10KN |
| 显示模式 | Mpa/KN可调 |
| 分辨率 | 0.01KN |
| 空心油缸行程 | 10mm |
| 测试误差 | 1% |
| 数据存储，和删除 | 有 |
| 峰值保持功能 | 有 |
| 液晶照明功能 | 有 |
| 折线修正 | 10段 |
| 支腿跨地 | 125mm |
| 外形尺寸 | 50*23*40mm |
| 主体材质重量 | 2kg |

三、产品特点：
♦采用进口合金材料，内置微型液压系统；
♦配有嵌入式数字压力仪表；
♦峰值保持，数据可记录、查询、删除操作；
♦数值10段折线修正，提高仪器精度；
♦超低功耗设计，无操作自动关机，连续工作时间可超过200小时；
♦强度和力值两种测量模式。
Product features:

♦ Imported alloy material and built-in micro hydraulic system;

♦ Equipped with embedded digital pressure gauge;

♦ Peak hold, data can be recorded, queried and deleted;

♦ 10-segment polyline correction to improve the accuracy of the instrument;

♦ Ultra-low power design, automatic shutdown without operation, continuous working time can exceed 200 hours;

♦ Two measurement modes of strength and force.

四、符合标准：
JGJ110-2008《建筑工程饰面砖粘结强度检验标准》
JGJ126-2000《外墙饰面砖工程施工及验收规程》
JGJ144-2004《外墙外保温工程技术规程》
JG158-2004 《胶粉聚苯颗粒外墙外保温系统》
JG149-2003 《膨胀聚苯板薄抹灰外墙外保温系统》
Fourth, meet the standards:

JGJ110-2008 "Test Standard for Bond Strength of Facing Bricks in Construction Engineering"

JGJ126-2000 "Code for Construction and Acceptance of Exterior Wall Facing Bricks"

JGJ144-2004 "Technical Regulations for External Thermal Insulation Engineering"

JG158-2004 "Plastic powder polystyrene particles for external wall exterior insulation system"

JG149-2003 "Extracted polystyrene board thin plaster external wall exterior insulation system"

五、产品配置：
♦主机1台
♦数字显示压力表1块（内置）
♦充电器1个
♦铝合金箱子1个
♦试块95*45mm/40*40mm各3块
♦AB胶1盒
♦说明书1份
♦合格证、保修卡、装箱单各1份
可选试块规格有：100*100mm、Φ50mm　　 特殊规格可定做
Five, product configuration:

♦ 1 host

♦ 1 digital display pressure gauge (built-in)

♦ 1 charger

♦ 1 aluminum alloy box

♦ Test pieces 95 * 45mm / 40 * 40mm, 3 pieces each

♦ AB glue 1 box

1 manual

♦ Certificate of conformity, warranty card, packing list

Optional test block specifications are: 100 * 100mm, Φ50mm special specifications can be customized