名称:推出法砂浆强度检测仪

其他名称：砌筑砂浆强度推出仪

型号：TC-1

荣计达产品编号：SJ34   5000元

推出法砂浆强度检测仪是依据国家标准GB/T50315《砌体工程现场检测技术标准》中“推出法”的技术要求所研制的测试砌筑砂浆强度的专用仪器。其使用方法是在砌体的一块砖上测试砌体的砂浆强度，将被测砖面及侧面的砂浆清除，把仪器安装在砖上手动加荷侧向推砖，当砖被推出时，由高精度的荷载传感器通过仪表峰值显示器将力值显示出来，然后换算为砂浆强度。

The launching mortar strength tester is a special instrument developed to test the strength of masonry mortars in accordance with the technical requirements of the "rolling out method" in the national standard GB / T50315 "Technical Standards for On-site Inspection of Masonry Engineering". The method of use is to test the strength of the mortar on a brick of the masonry, remove the mortar on the tested brick surface and the side, install the instrument on the brick and manually load the bricks laterally. The high-precision load sensor displays the force value through the instrument peak display, and then converts it into mortar strength.

推出法砂浆强度检测仪技术参数：

■额定推力：30KN

■相对测量范围：20～80％

■示值相对误差：±3％

■额定行程：80mm

■力值显示仪器A小分辨值：0.05KN

■力值范围：0～30KN

■具有测力峰值保持功能

■仪器读数显示稳定，在4h内的读数漂移小于0.05KN

■测点选择与布置：

（1）、测点宜均匀布置在墙上，并应避开施工中的预留洞口。

（2）、被推丁砖的承压面可采用砂轮磨平，并应清理干净。

（3）、被推丁砖下的水平灰缝厚度应为8～12mm。

（4）、测试前，被推丁砖应编号，并详细记录墙体的外观情况。

■外形尺寸：83X40X20mm

■重量：27kg

Technical parameters of mortar strength tester introduced:

■ Rated thrust: 30KN

■ Relative measurement range: 20 ～ 80%

■ Relative error of displayed value: ± 3%

■ Rated travel: 80mm

■ Force value display instrument A small resolution: 0.05KN

■ Range of force value: 0 ～ 30KN

■ With force peak holding function

■ The instrument reading display is stable, the reading drift within 4h is less than 0.05KN

■ Measurement point selection and layout:

(1) The measuring points should be evenly arranged on the wall, and the reserved openings during construction should be avoided.

(2) The pressure-bearing surface of the pushed brick can be smoothed with a grinding wheel and should be cleaned up.

(3) The thickness of the horizontal gray joint under the pushed brick shall be 8-12mm.

(4) Before the test, the pushed bricks should be numbered, and the appearance of the wall should be recorded in detail.

■ Dimensions: 83X40X20mm

■ Weight: 27kg