名称：地坪压痕试验仪

型号：YH-500

一、产品简介

适用于水泥基耐磨地坪系统、渗透型液体硬化地坪系统、水泥基自流平地坪系统、树脂整体面层地坪系统和普通混凝土地坪系统的硬度测量。该产品原理是对一定直径的钢球施加一定的试验载荷压入待测地坪表面，经规定的保持时间后，卸除试验载荷，测量待测地坪表面压痕直径。本产品具有外观新颖，操作简单，试验结果准确等特点。

1. Product introduction

It is suitable for the hardness measurement of cement-based wear-resistant floor systems, penetrating liquid hardening floor systems, cement-based self-leveling floor systems, resin monolithic surface floor systems and ordinary concrete floor systems. The principle of this product is to apply a certain test load to a steel ball of a certain diameter and press it into the surface of the floor to be tested. After a specified holding time, the test load is removed and the diameter of the indentation on the surface of the floor to be tested is measured. This product has the characteristics of novel appearance, simple operation and accurate test results.

二、技术参数：

1、钢球直径：  10±0.01mm

2、荷载重量：  10±0.1N

3、配重砝码：  500±5N

4、千分表精度： 0.001mm

5、千分表量程： 0-12.7mm

6、外形尺寸： 520X520X650mm

7、整机重量：120kg

2. Technical parameters:

1. Steel ball diameter: 10±0.01mm

2. Load weight: 10±0.1N

3. Counterweight: 500±5N

4. The accuracy of the dial indicator: 0.001mm

5. The range of the dial indicator: 0-12.7mm

6. Dimensions: 520X520X650mm

7. The weight of the whole machine: 120kg