|  | Elix® 3/5/10 Water Purification Systems The standard for analytical-grade water Produce Consistently-pure Type II Water from Tap Elix system water meets or exceeds Type II water quality (corresponding to analytical-grade water) as defined by CAP, CLSI and ISO® 3696/BS 3997. With easy operation and maintenance, Elix systems have set a new standard in the pure water market. With Elix systems, control of water purity is built-in to every step of the purification process – ensuring that water quality will be a constant in your applications – not an additional variable. Applications - Microbiological media preparation - Buffer preparation - Hydroponics - Manufacturing chemical and biochemical reagents - Purified water for pharmaceutical applications (according to US and European Pharmacopeia) - Feed for laboratory equipment (washing machines, clinical analyzers, stability chambers, humidifiers, autoclaves, weathering test equipment instruments, hydrogen gas generators) - Feed to Milli-Q® ultrapure water systems Features - A unique and easy-to-install prefiltration pack unit - Self-maintenance of the reverse osmosis membrane - Self-regeneration of the ion-exchange resins by an electrical current - Advanced reverse osmosis technology with high recovery loop reduces water consumption by more than 50% - Constant product flow rate - Integrated UV lamp for optimum water quality for applications sensitive to bacteria - All system functions are accessible from a user-friendly keypad and displayed on backlit screen Elix System Performance and Specifications (return to top) Elix 3 System Elix 5 System Elix 10 System Water Needs 10 to 60 L per day 50 to 100 L per day 100 to 200 L per day Flow Rate, L/h (± 15% at 7 °C< T <30 °C) 3 5 10 Resistivity, M·cm (compensated to 25 °C)* 5–15 5–15 5–15 Conductivity, µS/cm (compensated to 25 °C)* < 0.2 < 0.2 < 0.2 TOC, ppb <30 <30 <30 Bacteria Count**, cfu/mL <1 <1 <1 Silicate Removal, % >99.9 >99.9 >99.9 Water Recovery, % 15 18 24 Dimensions Height, cm (in.) 45.7 (18) 45.7 (18) 45.7 (18) Width, cm (in.) 25.5 (10) 25.5 (10) 25.5 (10) Depth, cm (in.) 31.5 (12.4) 31.5 (12.4) 31.5 (12.4) Operating Weight, kg (lb) 15 (33) 15 (33) 16 (35.3) *[CO2] ≤ 30 ppm in feedwater: typical resistivity 10 –15 M·cm [CO2] > 30 ppm in feedwater: typical resistivity > 2 M·cm **Valid for Elix systems with UV lamp Elix System Cartridge Selection Guide (return to top) Feedwater Fouling Index and Chlorine Level Integrated Softening Agent Bacteria Reduction Progard 1 Pretreatment Pack Low • Progard S1 Pretreatment Pack (bacteriostatic activated carbon) Low • • Progard 2 Pretreatment Pack (long) High • Progard S2 Pretreatment Pack (bacteriostatic activated carbon), long High • • Progard 1 Pretreatment Pack (without polyphosphate) Low Progard 2 Pretreatment Pack (without polyphosphate), long High |
| --- | --- |