Mini-BeadBeater-1™

Features

- Rapid and highly efficient.

- Totally Sealed - no dangerous aerosols.

- Simple to use.

- Disposable vials and beads - no sample cross-contamination.

- Very high energy shaking - superior to lab vortexers

- Versatile - use for up to 400 mg (wet weight) of bacteria, yeast, algae, tissue culture cells and plant and animal tissue.

Specifications

- Motor: 115 Volt A/C, 60 Hz, 0.6 amp, 3 wire grounded plug. (European 220 Volt version available)

- Dimensions: 5 inches W, 10 inches D, 7 inches H, shipping wt. 10 lbs

- Digital: Touch pad controls speed and length of homogenization.

- RPM: 2500, 4200, 4600, and 4800.

- Time Setting: 0-5 minutes in 10 second increments.

- Standard 2.0 ml microvials with screw-caps containing neoprene o-rings.

- Cell or tissue capacity up to 400 mg (wet weight)